## Slide 1: Wind Turbine Predictive Maintenance Platform
Demo by Umesh Nikam, AI/ML Engineer
8 October 2026

## Slide 2: Agenda
01
The Problem
02
What the Platform Does
03
What the Data Shows
04
Roadmap

## Slide 3: The Problem
A gearbox, hydraulic system or pitch motor usually gives a signal before it breaks: a slow temperature rise, a pressure drop, a change in vibration. Today nobody watches those signals closely enough to catch the problem early.
01
Turbines sit idle
The turbine stays down while a technician drives out and finds the fault by hand.
02
Emergency repairs cost more
Fixing a part after it breaks costs more than replacing it on a planned visit.
03
Parts fail completely
Parts run until they break instead of being swapped while they still had life left.

## Slide 4: What the Platform Does
01
Fault detection
Flags which of 7 components is showing trouble, from live sensor readings.
02
Remaining life (RUL)
Estimates how long a component has left, in days, months or years.
03
Trend forecasts
Shows where a reading is heading, with a P10 to P90 range.
04
Live alerts
Raises an alert the moment a reading or prediction crosses a set limit.
05
Fleet overview
Every turbine across all three farms on one screen, with health status.
06
Digital twin
A live view of each turbine, driven by its real sensor data.

## Slide 5: Built on Real Turbine Data
Everything is based on a public SCADA dataset from three real wind farms, including the maintenance notes written when something broke.
36
Turbines
3
Wind farms
44
Real failure events
7
Component categories

## Slide 6: How Each Component Fails
C1
Gearbox
Oil leaks or low oil pressure. Gears wear and heat up; oil sensors drift days before shutdown.
C2
Hydraulics
Leaks, worn accumulators or weak pumps. Pressure falls slowly and the pump runs more often.
C3
Pitch System
A blade motor or drive stops responding, so the turbine shuts down for safety.
C4
Generator
Bearings or windings wear out. Temperature alone can miss it if output has already dropped.
C5
Transformer
Overheating or pressure building in the oil. Oil temperature is the best early sign.
C6
Rotor Brake
Low hydraulic pressure means the brake can't grip. Pressure runs low before the fault.
C7
Bearing
The main bearing wears under the rotor's weight. Vibration shows it well before temperature does.
All
Common pattern
Every component gives a drifting signal days or weeks ahead. The platform catches that drift.

## Slide 7: Each Farm Fails Differently
A
Farm A
Hydraulic, gearbox, generator and transformer faults. Matches its documented fault list exactly. No pitch faults at all.
5
Turbines
11
Failure events
B
Farm B
Main bearing damage is the real issue and needs vibration sensors to catch. Some of its events still sit outside the 7 categories.
9
Turbines
6
Failure events
C
Farm C
Pitch and blade-angle faults lead, with 8 events. It controls each of its three blades separately, so this fits.
22
Turbines
27
Failure events

## Slide 8: How It Works
S1
Collect
Each turbine sends temperature, pressure and vibration readings.
S2
Clean
Readings are checked, cleaned and grouped by component (bronze, silver, gold).
S3
Predict
Trained models flag faults and estimate remaining life.
S4
Show
Dashboard shows fleet health, forecasts and alerts in one place.
Live demo screens
D1
Fleet Overview
All turbines at a glance
D2
Asset Detail
One turbine's sensor history
D3
Forecasts & RUL
Where a component is heading
D4
Alerts
What's flagged and why

## Slide 9: Status and Roadmap
Today
Full stack running locally on Docker
Real pipeline and model training on all 3 farms
Dashboard with RUL, forecasts and alerts
Digital twin shows live data (not a physics model)
Next
Deploy the pipeline to AWS
Retrain as new fault events come in
Better vibration features for Farm B bearings
Future Phase
Work orders linked to alerts
Maintenance scheduling from RUL
More sensor types and farms

## Slide 10: Thank You
Questions and next steps
8 October 2026